## Slide 1: Lecture 5-1 Custom IP, XDC, Linker, Lab #4
IP Creation and Repository
  IP Creation
  IP Editing
  IP Repository Location in Project Settings
Lab #4-1 AXI4-Lite Slave Custom IP:
  led_ip\ip_repo\led_ip_1.0\hdl: led_ip_v1_0.v, led_ip_v1_0_S_AXI
  led_ip\ip_repo\led_ip_1.0\drivers\led_ip_v1_0\src
Lab #4-2 Explained
XDC – Xilinx Design Constraints
Block RAM Generator IP for Zynq-7010
Standard ARM Programming Model
Linker Script and Address Management
Clock Configurations from ps7_init.html file
Board Support Package for led_ip

## Slide 2: Assignment
Lab #4 Part 1: ZYNQ Lab 3 Use Vivado to Build Embedded Systems, pages ZYNQ3-1 to ZYNQ3-16.
Lab #4 Part 2: ZYNQ Lab 4 Adding IP Cores in PL, pages ZYNQ2-1 to ZYNQ2-16. Demonstrate this part to get credit for this lab.
References

## Slide 3: IP Cores and Custom IP Blocks
Intellectual Property (IP) refers to preconfigured logic functions that can be used in your design.
An IP contains its hardware design and software driver.
A core IP is provided by Xilinx and a custom IP is created by user.
All IP available in the Vivado IP Catalog can be used to create IP Integrator designs
Any IP Integrator block design can be quickly packaged as a single complex IP
IP repository

## Slide 4: IP Files, IP Packager, IP Repositories
IP files
  Sources
  Simulation files
  Examples
  Test bench
  Documentation
  Driver
IP Packager
  Create and edit IP
IP Repository is a storage location for all IP files

## Slide 5: IP Packager
Automatically analyse project/files to determine parameters
Initial Summary
Identifies
  Files
    Source HDL, Testbenches, Documentation,
  Parameters
    Configurable
  Ports
  Interfaces
  Compatibility
Creates GUI Layout for IPI

## Slide 6: Example IP Core and Custom IP
AXI Interface IP core from library
  Source
  Simulation models
  Documentation
  Test bench
  Example designs
  driver
Custom IP design with AXI interface
IP Packager
Source (C, RTL, IP, etc)
Simulation Models
Documentation
Example Designs
Test Bench
Vivado IP Integrator
Standardized IP-XACT representation
IP Catalog
3rd Party IP
Xilinx IP
User IP

## Slide 7: Files Created for an IP Component
bd - Block Diagram tcl file
drivers
  SDK and software files (c code)
hdl - Verilog/VHDL code (should be inside project directory)
src – source code for the IP component
xgui - GUI tcl file to represent the layout symbol of IP
component.xml IP XACT description

## Slide 8: Edit IP in Block Design
To edit an IP in a block design
Right click on an IP instance on Block Design to choose Edit IP in Packager to open a new Vivado project
Template files have been generated and are added to the project
IP can now be edited
  Modify existing template files, add user source files
IP Packager will be open
  Last step is to Package IP

## Slide 9: Add an IP from Repository to Your Project
To add an IP to your project
  Start Project Settings
  Choose IP icon
  IP directory will not change
I prefer to copy an IP to its user’s folder so that the IP will not be misplaced.

## Slide 10: IP-XACT
Industry Standard (IEEE) XML format to describe IP using meta-data
  Ports
  Interfaces
  Configurable Parameters
  Files, documentation
IP-XACT only describes high level information about IP, not low level description, so does not replace HDL or Software.
Enables automatic connection, configuration and integration
Enables integration of 3rd Party IP
  (And Export of your own IP)

## Slide 11: Component.xml for led_ip_1.0

## Slide 12: *.tcl files
TCL, Tool Command Language , is a file extension for a script written in TCL.
Tool Command Language (TCL) is a dynamic open source language used for building web and desktop applications. Whether on Windows, Mac OS X, or Linux operating systems, TCL files can be opened and edited by WISH and TCLSH.
https://en.wikipedia.org/wiki/Tcl
Notes: Tcl (pronounced "tickle" or tee cee ell /ˈtiː siː ɛl/[6]) is a high-level, general-purpose, interpreted, dynamic programming language. It was designed with the goal of being very simple but powerful.[7] Tcl casts everything into the mold of a command, even programming constructs like variable assignment and procedure definition.[8] Tcl supports multiple programming paradigms, including object-oriented, imperative and functional programming or procedural styles.
It is commonly used embedded into C applications,[9] for rapid prototyping, scripted applications, GUIs, and testing.[10] Tcl interpreters are available for many operating systems, allowing Tcl code to run on a wide variety of systems. Because Tcl is a very compact language, it is used on embedded systems platforms, both in its full form and in several other small-footprint versions.[11]

## Slide 13: Lab #4 Part 1: Adding Custom IP to the System, XUP ZYNQ 3
Lab #4 Part 1: ZYNQ Lab 3 Use Vivado to Build Embedded Systems, pages ZYNQ3-1 to ZYNQ3-16.
Lab #4 Part 2: ZYNQ Lab 4 Adding IP Cores in PL, pages ZYNQ2-1 to ZYNQ2-16. Demonstrate this part to get credit for this lab.
Create and Package IP
Generates HDL template for
  Slave/Master
    AXI Lite/Full/Stream
Optionally Generates
  Software Driver
    Only for AXI Lite and Full slave interface
  Test Software Application

## Slide 14: Lab #4 Part 1: Adding Custom IP to the System, XUP ZYNQ 3
The User IP in led_ip_v1_0.v contains a register to store LED data
The IP is clocked and reset by PS
LEDs themselves do not store data
8-bit output
AXI Interconnect
AXI4-Lite IP (Slave)
AXI Transaction logic
(Ready, Valid, Response)
Write Response
Read Addr
Read Data
Write Data
Write Addr
Registers
led_ip_v1_0_S_AXI.v
led_ip_v1_0.v
lab3_user_logic.v
User IP
8-bit LED Register

## Slide 15: Create an AXI Lite IP from the AXI Lite Template
HDL implementation of AXI Interface is available
  32 bit data width
User specifies required number of registers (minimum 4)
Read/write to/from Registers implemented
User logic can be easily connected
User logic can be a hierarchical design

## Slide 16: A Generated Template for AXI LED

## Slide 17: Subroutines in its Driver Library

## Slide 18: AXI4-Lite Slave Custom IP: led_ip_v1_0.v
S_AXI bus- standard template
axi_aclk
  System clock from PS
Axi_aresetn
  System reset from PS
LED[3:0]
  custom port

## Slide 19: Three Levels: led_ip_v1_0.v, led_ip_v1_0_S_AXI, lab3_user_logic
Top: led_ip_v1_0.v – the wrapper
AXI: led_ip_v1_0_S_AXI – Verilog module
  Slave axi4 standard template
Custom: lab3_user_logic – user IP circuit in led_ip_v1_0_S_AXI.v
  8-bit LED register to store data
Under IP Editor for led_ip_v1_0

## Slide 20: AXI4-Lite Slave IP: led_ip_v1_0.v, led_ip_v1_0_S_AXI, lab3_user_logic
This view is generated by Xilinx ISE tools to see three levels of modules
LED wires need to be declared on all three levels.
lab3_user_logic

## Slide 21: AXI4-Lite Slave IP: led_ip_v1_0.v, led_ip_v1_0_S_AXI, lab3_user_logic
This view is generated by Elaborated Design under RTL Analysis
lab3_user_logic
lab3_user_logic

## Slide 22: AXI4-Lite Slave IP: module led_ip_v1_0.v
With IP Editor: Run RTL Analysis->Schematic to obtain schematic
4-bit addresses for read s_axi_araddr[3:0] and write s_axi_awaddr[3:0]
8-bit LED LED[7:0], which is a changeable parameter
32-bit read and write data busses

## Slide 23: AXI4-Lite Slave IP: , led_ip_v1_0_S_AXI
This is a standard axi4-lite slave module template
lab3_user_logic module is inserted into this template to create a custom IP

## Slide 24: AXI4-Lite Slave IP: module lab3_user_logic
Create an 8 bit register to store 8-bit data of 32-bit Write Data from axi slave interface
This 8-bit data can be displayed on LEDs
Reset by S_AXI_ARESETN
Clocked by S_AXI_ACLK
Enabled by slv_reg_wren and axi_asaddr==3’h0, 12 bit address
Take 8 bits of 32 bit data on S_AXI_WDATA
Notice the magic numbers!

## Slide 25: AXI4-Lite Slave IP: lab3_user_logic module, 3 level deep
lab3_user_logic.v under led_ip_v1_0_S_AXI.v
lab3_user_logic

## Slide 26: One Instance of led_ip_v1_0.v with four LEDs
System_led_ip_0_0.v == led_ip_v1_0.v, notice LED[3:0]
These Schematics are generated with Xilinx ISE

## Slide 27: One Instance of led_ip_v1_0.v with four LEDs
System_led_ip_0_0.v == led_ip_v1_0.v, notice LED[3:0]
lab3_user_logic.v is in led_ip_v1_0_S_AXI_inst

## Slide 28: led_ip_v1_0 IP folder: Hardware and Driver
Three folders
  ip_repo (repository folder)
  led_ip_0
  Managed_ip_project
hdl folder in led_ip_0 folder
  led_ip_v1_0.v
  Led_ip_v1_0_s_AXI.v
driver folder in led_ip_0 folder
  led_ip.c
  led_ip.h
  led_ip_selftest.c
  Makefile

## Slide 29: led_ip_v1_0 Driver files
Driver files are exported to SDK as part of board support package *.bsp folder
led_ip.c - #include "led_ip.h"
led_ip.h
  #define LED_IP_mWriteReg(BaseAddress, RegOffset, Data) \ Xil_Out32((BaseAddress) + (RegOffset), (u32)(Data))
  #define LED_IP_mReadReg(BaseAddress, RegOffset) \ Xil_In32((BaseAddress) + (RegOffset))
  XStatus LED_IP_Reg_SelfTest(void * baseaddr_p);
led_ip_selftest.c
Makefile

## Slide 30: Lab #4 Part 2: Writing Basic Software Application and Block RAM
Read and display slide switches and buttons on terminal 1
Send slide switch values to LEDs
Change memory allocation by linker Script
Lab #4 Part 1: ZYNQ Lab 3 Use Vivado to Build Embedded Systems, pages ZYNQ3-1 to ZYNQ3-16.
Lab #4 Part 2: ZYNQ Lab 4 Adding IP Cores in PL, pages ZYNQ2-1 to ZYNQ2-16. Demonstrate this part to get credit for this lab.
ARM
Cortex-A9
DDR3
Memory
Controller
AXI
Interconnect
Block
AXI-BRAM Controller
Memory
GPIO
UART
RS232
DIP Switches
AXI4
AXI4-Lite
AXI4-Lite
GPIO
LED_IP
Push-Buttons
AXI4-Lite
LED
BRAM
M_AXI_GP0
PS
PL

## Slide 31: Lab #4 Part 2: Block Design: Use One Instance of led_ip
Notice led_ip_v1_0.v has been wrapped by one more higher level system wrapper: system_led_ip_0_0.v
System_led_ip_0_0.xci
  The XCI file is an IP-XACT component instance XML file that records the values of project options, customization parameters, and port parameters used to create the IP. From page 14, ug895-vivado-system-level-design-entry.pdf

## Slide 32: Three Levels of led_ip_v1_0.v IP with four LEDs
system_led_ip_0_0.v from
  C:\Xilinx\embedded\2015_2_zynq_labs\lab4\lab4.srcs\sources_1\bd\system\ip\system_led_ip_0_0\synth
led_ip_v1_0.v and led_ip_v1_0_S_AXI.v from
  C:\Xilinx\embedded\2015_2_zynq_labs\led_ip\ip_repo\led_ip_1.0\hdl
lab3_user_logic.v from
  C:\Xilinx\embedded\2015_2_zynq_labs\led_ip\ip_repo\led_ip_1.0\src
Xilinx ISE

## Slide 33: Xilinx Design Constraints (XDC) File for Zybo: Master XDC zip
A zipped file called ZYBO_Master.xdc is available from https://github.com/Digilent/ZYBO/tree/master/Resources/XDC.
Here is the header of ZYBO_Master.xdc

## Slide 34: Add constraints file lab3_zybo.xdc
Xilinx Design Constraints (XDC) File
Specify pin positions where LEDs are located
PACKAGE_PIN is a property followed by a physical pin number
get_ports applies the property to a logical port
############################
# On-board LED #
############################
set_property PACKAGE_PIN M14 [get_ports LED[0]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[0]]
set_property PACKAGE_PIN M15 [get_ports LED[1]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[1]]
set_property PACKAGE_PIN G14 [get_ports LED[2]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[2]]
set_property PACKAGE_PIN D18 [get_ports LED[3]]
set_property IOSTANDARD LVCMOS33 [get_ports LED[3]]

## Slide 35: Lab #4 Part 2: top Level Circuit
buttons and switches are standard S_AXI4 lite interfaces
led_ip_0 and axi_bram_ctrl_0 are custom IP S_AXI4 interfaces

## Slide 36: Lab #4 Part 2: top Level Circuit
buttons and switches are standard S_AXI4 lite interfaces
led_ip_0 and axi_bram_ctrl_0 are custom IP S_AXI4 interfaces

## Slide 37: Block RAM Generator IP for Zynq-7010
AXI Block RAM controller IP, AXI4 Slave
Block RAM IP, Single Port RAM
36Kb block RAM x 60 blocks
True dual-port
Up to 72 bits wide
Configurable as dual 18 Kb block RAMs

## Slide 38: Synchronous Dual-Port and Single-Port RAMs (UG473 7 Series FPGAs Memory Resources)
Two independent access ports
No arbitration between the ports
Write conflict will not cause physical damage but may cause data loss
Zynq-2010 BRAM: 36Kbx60=2.16Mb
In FPGA area

## Slide 39: Standard ARM Programming Model
Processing system and programmable logic look the same
  AMBA® and AXI interfaces
  Memory-mapped I/O
  Register access
Consistency for PS and PL = ease of use
Memory map usage: total of 4 GB
  1 GB: DDR RAM
  2 GB: dedicated to PL peripherals
  1 GB: PS peripherals, on-chip memory (OCM), external flash

## Slide 40: Programmer’s View of Programmable Logic
Programmable logic (PL) memory map
  2 GB total space
    1 GB for each AXI master: GP0, and GP1
  Accessible from any processing system (PS) master
    Either Cortex-A9 CPU
    PS DMA engine
    PS peripheral DMA engine
    Ethernet
    USB
    SD/SDIO
Code Snippet
Custom Peripheral

## Slide 41: Address Management
Embedded processor design requires managing the following:
  Address map for the peripherals
  Location of the application code in the memory space
    Block RAM
    SRAM
    External memory (Flash, DDR3)
Memory requirements are based on the following:
  The amount of memory required for storing instructions
  The amount of memory required for storing data associated with the program
Executables and static data must be allocated in On-Chip RAM or DRAM
Heap and stack can be allocated in Block RAM

## Slide 42: Linker and Locator Flows
.text contains executable code
.data segment contains initialized data
.bss segment contain uninitialized data
.text1
.data1
.bss1
foo1.o
foo2.o
0x0000
0x0FF0
0xFFFF
0xF000
Locate
Merged Output Sections
Heap
Executable Image
.text Code
.bss uninitialized data
.data Initialized data
.text2
.data2
.bss2
Link
.text
.data
.bss
Stack

## Slide 43: Linker Properties and Linker Script
The Root panel displays properties for the selected configuration
Shown are the linker options for the Debug configuration
Default settings are fine for simple applications
Linker script controls the linking process
  Map the code and data to a specified memory space
  Set the entry point to the executable
  Reserve space for the stack
Required if the design contains a discontinuous memory space

## Slide 44: SDK Project: Linker Script
Application Software Project
  A code
  Linker script file
Board Support Package *.bsp
Hardware Platform – system_wrapper
Linker Script

## Slide 45: Linker Script Generator GUI and File lscript.ld
Launch from Xilinx Tools > Generate Linker Script, or from the C/C++ perspective, right-click on <project> > Generate Linker Script
Table-based GUI allows you to define the memory space for code and data sections
The tool will create a new linker script (the old script is backed up)
C:\Xilinx\embedded\2015_2_zynq_labs\lab4\lab4.sdk\lab4\src\lscript.ld

## Slide 46: Linker Script Generator GUI
Notice the base address and size of each memory block
Both RAM blocks and DDR RAM can be used to store executable and static data
DDR2 memory size is 511MB
Block RAM size is 8KB and operates
RAM_0 is 192KB and RAM_1 is about 64 KB
File location: C:\Xilinx\embedded\2015_2_zynq_labs\lab4\lab4.sdk\lab4\src\lscript.ld

## Slide 47: Board Support Package Macros for led_ip in led_ip.h
#ifndef LED_IP_H
#define LED_IP_H
/****************** Include Files ********************/
#include "xil_types.h"
#include "xstatus.h"
#define LED_IP_S_AXI_SLV_REG0_OFFSET 0
#define LED_IP_S_AXI_SLV_REG1_OFFSET 4
#define LED_IP_S_AXI_SLV_REG2_OFFSET 8
#define LED_IP_S_AXI_SLV_REG3_OFFSET 12
#define LED_IP_mWriteReg(BaseAddress, RegOffset, Data) \
Xil_Out32((BaseAddress) + (RegOffset), (u32)(Data))
#define LED_IP_mReadReg(BaseAddress, RegOffset) \
Xil_In32((BaseAddress) + (RegOffset))
XStatus LED_IP_Reg_SelfTest(void * baseaddr_p);

## Slide 48: Xil_Out32(), Xil_in32() in standard_v4_2/src/xil_io.c
/* Performs an input operation for a 32-bit memory location by reading from the
* specified address and returning the Value read from that address.
** @paramAddr contains the address to perform the input operation at.
* @returnThe Value read from the specified input address.
* @noteNone. */
u32 Xil_In32(u32 Addr)
{
return *(volatile u32 *) Addr;
}
/* Performs an output operation for a 32-bit memory location by writing the
* specified Value to the specified address.
* @paramOutAddress contains the address to perform the output operation at.
* @paramValue contains the Value to be output at the specified address.
* @returnNone.
* @noteNone */
void Xil_Out32(u32 OutAddress, u32 Value)
{
*(volatile u32 *) OutAddress = Value;
}
Read (return) content at address Addr
Write (store) Value to content at address Addr
Level 0 Driver

## Slide 49: LED device defined in xparameters.h
/* Definitions for driver LED_IP */
#define XPAR_LED_IP_NUM_INSTANCES 1
/* Definitions for peripheral LED_IP_0 */
#define XPAR_LED_IP_0_DEVICE_ID 0
#define XPAR_LED_IP_0_S_AXI_BASEADDR 0x43C00000
#define XPAR_LED_IP_0_S_AXI_HIGHADDR 0x43C0FFFF

## Slide 50: Lab #4 Part 2: main() to display slide switch values on LEDs
#include "xparameters.h"
#include "xgpio.h"
#include "led_ip.h"
int main (void)
{
XGpio dip, push;
int i, psb_check, dip_check;
xil_printf("-- Start of the Program --\r\n");
XGpio_Initialize(&dip, XPAR_SWITCHES_DEVICE_ID);
XGpio_SetDataDirection(&dip, 1, 0xffffffff);
XGpio_Initialize(&push, XPAR_BUTTONS_DEVICE_ID);
XGpio_SetDataDirection(&push, 1, 0xffffffff);
while (1) {
psb_check = XGpio_DiscreteRead(&push, 1);
xil_printf("Push Buttons Status %x\r\n", psb_check);
dip_check = XGpio_DiscreteRead(&dip, 1);
xil_printf("DIP Switch Status %x\r\n", dip_check);
LED_IP_mWriteReg(XPAR_LED_IP_S_AXI_BASEADDR,0,dip_check);
for (i=0; i<9999999; i++); }
}

## Slide 51: Three Linker Memory Options: Internal RAM, Block RAM, DDR RAM
ps7_ram_0_S_AXI_BASEADDR, fastest, internal RAM in PS based at 0x00000000 or 0xFFFF0000
ps7_ddr_0_S_AXI_BASEADDR, faster, external DDR memory based at 0x00100000
axi_bram_ctrl_0, slow, very slow – internal block RAM in PL based at 0x40000000

## Slide 52: Memory Clock Speeds: Internal, Block RAM, DDR
650MHz - ps7_ram_0_S_AXI_BASEADDR
525MHz - ps7_ddr_0_S_AXI_BASEADDR
100MHz - axi_bram_ctrl_0

## Slide 53: Clock Configurations from ps7_init.html file on SDK
Click on ps7_init.html in bsp folder
Click CLK Configuration to see (1) crystal speed, (2) CPU speed, (3) UART speed, (4) four FPGA clock speed
Click DDR Configuration to see DDR clock speed

## Slide 54: Memory Allocation
Heap and Stack in BRAM: axi__bram_ctrl_0_S_AXI_BASEADDR=0x4000000
Code and Data in DDR: ps7_ddr_0_S_AXI_BASEADDR=0x0010000

## Slide 55: Object Dump: lab4.elf
C:\Xilinx\embedded\2016_2_zynq_labs\lab4\lab4.sdk\lab4\Debug
  lab4.elf
Open a command shell
>under command shell: arm-Xilinx-eabi-objdump –h lab4.elf

## Slide 56: Object Dump: arm-xilinx-eabi-objdump –h lab4.elf
C:\Xilinx\embedded\2016_2_zynq_labs\lab4\lab4.sdk\lab4\Debug
Header information, memory map, Data, Disassemble code
Section
Name
Loadable Memory Address
Virtual Memory Address
Section Size
Byte alignment
Offset from the beginning of the section header table

## Slide 57: Heap and Stack in BRAM, Data and Code in DDR
Code .text in DDR starting at 0x00100000
Data
Heap in BRAM starting at 0X4000000
Stack in BRAM starting at 0X4000400