## Slide 1: Lecture9 ARM I2C Modules
References
I2C Standard
TMP101 Temperature Sensor
ARM I2C Modules
Lab #9 Part 1: Connecting Two TMP101 Sensors to Zybo on MIO and SelectIO
Xilinx I2C Software Driver Library
My Template Code for Lab #9 Part 1
I2C Controller Module of Zynq 7000

## Slide 2: ARM I2C Module References
Chapter 20 I2C Controller, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585 (v1.10) February 23, 2015
Xilinx Processor IP Library – iicps_v3_0 C:\Xilinx\SDK\2015.2\data\embeddedsw\XilinxProcessorIPLib\drivers\iicps_v3_0
ARM CPU
I2C 1
I2C 0
tmp101
tmp101
SCK
SCK
SDA
SDA
MIO
Select IO

## Slide 3: I2C is a 2-Wire Serial Bus (plus the common voltage reference wire)
SDA – Serial Data Line
SCL – Serial Clock Line
Ground – common voltage reference line
Two pull-up resistors of 4.7kΩ for open drain outputs

## Slide 4: Start and Stop Conditions
Start condition is when SCL=1 and SDA goes from 1 to 0
Stop condition is when SCL=1 and SDA goes from 0 to 1
Notice data line SDA cannot change when SCL=1 to set data values because SDA change indicates Start or Stop when SCL=1.

## Slide 5: Data Transfer
I2C bus is idle when both SDA and SCL are high “1” or hi-Z
Data transfer starts after Start Bit appears
Each frame after Start Bit is 9 bits long: eight bit data and one bit acknowledgement
Data transfer may continue until Stop Bit appears

## Slide 6: An Example Data Transfer Sequence

## Slide 7: The First Byte Is Composed of 7-bit Address and bit
Slave address is 7 bits long
The least significant bit is Read (“1”) or Write (“0”) bit to inform the device at the address to be ready for read or write operation

## Slide 8: TMP101 Digital Temperature Sensor With I2C from TI
Features
  DIGITAL OUTPUT: I2C Serial 2-Wire
  RESOLUTION: 9- to 12-Bits, User-Selectable
  ACCURACY:
  ±2.0°C from −25°C to +85°C (max)
  ±3.0°C from −55°C to +125°C (max)
  LOW QUIESCENT CURRENT:
  WIDE SUPPLY RANGE: 2.7V to 5.5V
  TINY SOT23-6 PACKAGE
Three Addresses
  ADD0=0V: 7’b1001000
  ADD0=5V: 7’b1001010
  ADD0 floating: 7’b1001001
Alert Pin
  One-shot conversion
  Limits Status Warning
Notes: OS/ALERT (OS)
The TMP100 and TMP101 feature a One-Shot
Temperature Measurement Mode. When the device is in
Shutdown Mode, writing a 1 to the OS/ALERT bit will start
a single temperature conversion. The device will return to
the shutdown state at the completion of the single
conversion. This is useful to reduce power consumption in
the TMP100 and TMP101 when continuous monitoring of
temperature is not required.
Reading the OS/ALERT bit will provide information about
the Comparator Mode status. The state of the POL bit will
invert the polarity of data returned from the OS/ALERT bit.
For POL = 0, the OS/ALERT will read as 1 until the
temperature equals or exceeds THIGH for the programmed
number of consecutive faults, causing the OS/ALERT bit
to read as 0. The OS/ALERT bit will continue to read as 0
until the temperature falls below TLOW for the programmed
number of consecutive faults when it will again read as 1.
The status of the TM bit does not affect the status of the
OS/ALERT bit.

## Slide 9: TMP101 Temperature Registers Byte 1 and Byte 2
Two byte left aligned
Up to 12-bit resolution
  Byte 1 and D7-4 of Byte 2
Bit D0 of Byte 1 represents , T4
Reading Byte 1 is sufficient to obtain resolution, T11-4
The smallest resolution T0 of TMP101 is bit D4 of Byte 2:

## Slide 10: TMP101 Pointer Register
Pointer Register
  Stores address of register to be accessed
Temperature
  12 bits in two Bytes 1 and 2
Configuration
TLOW
THIGH

## Slide 11: TMP101 Configuration Register
Configuration
  R1 and R0 are resolution bits to change speed and resolution
  OS/ALERT is Special event alert output
  F1 and F0 are Fault Queue bits to set triggering tolerance
  POL is Polarity of Alert Active Mode
  TM is Thermostat Mode: comparator mode or interrupt mode
  SD is Shut Down Mode to save power instead of continuous conversion
TLOW and THIGH are two upper and lower limit registers

## Slide 12: TMP101 Reading

## Slide 13: I2C Command Sequence to Read TMP101 at 1001010
To read temperature
  Start
  0b10010101 //Send Device Address and Read Operation
  Receive the higher byte of Temperature
  Receive the lower byte of Temperature
  Stop
To set pointer register
  Start
  0b10010100 //Send Device Address and Write Operation
  0b00000011 //pointer register =2 for THIGH Register
  Write to lower byte of THIGH Register
  Write to higher byte of THIGH Register
  Stop

## Slide 14: TMP101 Breakout Board Circuit Schematic with Nexys 3 Board
TMP101 breakout board
Pin 1 SCL
Pin 2 SDA
Pin 3 GND
Pin 4 V+

## Slide 15: TMP101 I2C Waveforms: Slave Address=7’b1001001
Acknowledgment

## Slide 16: TMP101 I2C Waveforms: Temperature and Stop
Temperature
8’b00011000
20 Celsius
Stop

## Slide 17: Two I2C Modules of ARM Processing Systems

## Slide 18: Hardware View
ARM CPU
Lookup Table-> I2C 0
Loopup Table-> I2C 1
I2C 1 Module
Clock Frequency
I2C 0 Module
Clock Frequency
TMP101, Res=12b
Address= GND
0b1001000
Tmp101, Res=10b
Address=FLOATING
0b1001001
SCK
MIO 14
JF9
SCK
SelectIO
JB4 W20
SDA
MIO 15
JF10
SDA
SelectIO
JB3 V20
Device ID
Device ID

## Slide 19: Lab #8: Zynq 7000 MIO at a Glance and I2C 0 and I2C 1 MIO Pins
I2C 0 (SCK,SDL):
  10-11, 14-15, 18-19
  22-23, 26,27, 30-31, etc.
I2C 1 (SCK,SDL)
  12-13, 16-17, 20-21
  24-25, 28-29, 32-33, etc.
Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 20: Lab #8: Two TMP101 Breakout Boards on MIO and EMIO with ARM I2C Modules
Create a Zynq block design and double click it to open Re-Customized IP menu. Choose Peripheral IO Pins
Select I2C 0 to be connect to MIO pins 14 and 15 on PS
Select I2C 1 to be connect on EMIO through PL, terminal IIC_1
Bit stream file is needed to create interconnect for Select IO pins
Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 21: Lab #8: Connecting TMP101 Sensors to Zybo through MIO and SelectIO
TMP101PS - SCL, SDA, GND, V+ to JF9, JF10, JF11, JF12 on MIO
  JF9=MIO14 SDL, JF10=MIO15 SCK, MIO pins
TMP101PL - SCL, SDA, GND, V+ to JB3, JB4, JB5, JB6 on EMIO
  JB3=V20, JB4=W20, SelectIO pins

## Slide 22: Lab #8: Vivado Block Design and Xilinx Design Constraint File
Notice I2C 1 is accessible on the ZYNQ block
Choose IIC_1 IO to make it external
Run “Synthesize” and then assign SelectIO pins to I2C 1 pins. Save Xilinx Design Constraints file *.xdc
Generate bit stream file for Select IO interconnect network

## Slide 23: Lab #8: Choose SelectIO Pins for I2C 1
After Synthesis is done, open Synthesized Design and choose Layout->I/O Planning to see I/O Ports and pin assignments
Notice I2C 0 pins are assigned to Fixed-IO pins
Assign Pin V20 to I2C 1 clock pin and Pin W20 to I2C 1 data pin.
Save Design Constraint file (.xdc) generated for pins V20 and W20

## Slide 24: Lab #8: XDC File and xparameters.h
Save Xilinx Design Constraint (XDC) file for pins V20 and W20
Generate the bit stream file
Export hardware with the bit steam file
Launch SDK to see two I2C devices defined in xparameters.h
Program FPGA and Run Launch on hardware (GDB) to read temperatures
Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 25: Software View
ARM CPU
Lookup Table
I2C Driver
I2C
Instance 1
I2C
Instance 0
Res=12b
Address=0b1001000
Res=10b
Address=0b1001001
Device ID

## Slide 26: Lab #8: Two TMP101 Breakout Boards on Zybo Board
TMP101A on MIO on PS
  12 bit resolution
  Minimum temperature is
TMP101B on EMIO on PL
  10 bit resolution
  Minimum temperature is

## Slide 29: I2C Level 1 Software Driver in the PS Block: iicps v3_0
C:\Xilinx\SDK\2015.2\data\embeddedsw\XilinxProcessorIPLib\drivers\iicps_v3_0.
Support I2C hardware controller in the PS block
Base Addresses of I2C 0 and I2C 1 are fixed at (UG585)
  0xE0004000
  0xE0005000
I2C software driver in the PS block
  either a master or a slave on the IIC bus.
  supports both interrupt mode transfer and polled mode transfer
  Only 7-bit address is used in the driver, although the hardware also supports 10-bit address.

## Slide 30: I2C Master Operation Functions
Device Lookup – XIicPs_LookupConfig(Device ID);
Device configuration – XIicPs_CfgInitialize ();
Device test – XIicPs_SelfTest(Device ID);
Set Clock Speed – XIicPs_SetSClk(Device ID, Clock);
Check for Bus - XIicPs_BuIsBus(Device ID);
Blocking Write to slave - XIicPs__MasterSendPolled();
  wait until slave receives data
Blocking Read from slave - XIicPs__MasterRecvPolled();
  wait until slave sends data

## Slide 31: Blocking Write to Slave - XIicPs__MasterSendPolled();
8 bits
8 bits
8 bits
8 bits
ByteCount

## Slide 32: Blocking Read from Slave - XIicPs__MasterRecvPolled();
8 bits
8 bits
8 bits
8 bits
ByteCount

## Slide 33: Example of I2C Master Configuration
Define an I2C hardware module ID
  #define IIC_DEVICE_ID XPAR_XIICPS_0_DEVICE_ID
Define an instance of I2C device
  XIicPs Iic;
Configure I2C device
  XIicPs_Config *Config; int status;
  Config = XIicPS_LookupConfig(Iic); status = XIicPs_CfgInitialize(&Iic, Config, Config->BaseAddress);
Perform self test
  status = XIicPs_Selftest(&Iic); if(status!=XST_SUCCESS) return XST_FAILURE;
Set Clock Speed in Hz
  status = XIicPs_SetSClk(&Iic, ClockFreq in Hz);

## Slide 34: Example of I2C Master Configuration
Check if Bus is Busy
  while(XIicPs_BusIsBusy(&Iic));
Blocking write two bytes to send resolution to be 11 bits
    u8 resolution[2]={0b00000001,0b01000000); //pointer+data
    XIicPs_MasterSendPolled(&Iic, resolution, 2, Slave address);

## Slide 35
XIicPs tmp101a;
XIicPs_Config *tmp101a_config;
typedef struct {
u16 DeviceId; /**< Unique ID of device */
u32 BaseAddress; /**< Base address of the device */
u32 InputClockHz; /**< Input clock frequency */
} XIicPs_Config;
typedef struct {
XIicPs_Config Config;/* Configuration structure */
u32 IsReady;/* Device is initialized and ready */
u32 Options;/* Options set in the device */
u8 *SendBufferPtr;/* Pointer to send buffer */
u8 *RecvBufferPtr;/* Pointer to recv buffer */
int SendByteCount;/* Number of bytes still expected to send */
int RecvByteCount;/* Number of bytes still expected to receive */
int CurrByteCount;/* No. of bytes expected in current transfer */
int UpdateTxSize;/* If tx size register has to be updated */
int IsSend;/* Whether master is sending or receiving */
XIicPs_IntrHandler StatusHandler; /* Event handler function */
void *CallBackRef;/* Callback reference for event handler */
} XIicPs;

## Slide 36: My I2C Template Code: lab8I2ConARM_template.c
Hardware Device Definitions in xparamenters.h
Two Device instances: XIicPS temp101Aps, temp101Bpl;
  PS – tmp101 on MIO
  PL – tmp101 on SelectIO

## Slide 37: main()
printf("\r\nTMP101 on EMIO JF = %8.4f Celsius %8.4f Fahrenheit", temp1, 32+temp1*9/5);

## Slide 38: ReadTemperature() and ConfigureTMP101()

## Slide 39: ConfigureI2Cinstance()

## Slide 40: XIicPS_Lookupconfig() and XIicPs_CfgInitialize()
XIicPs_LookupConfig(DeviceId)
  Use the device identifier to find the static configuration structure defined in xiicps_g.c. This is setup by the tools. For some operating systems the config structure will be initialized by the software and this call is not needed.
XIicPs_CfgInitialize(InstancePtr, CfgPtr, EffectiveAddr)
  Uses a configuration structure provided by the caller. If running in a system with address translation, the provided virtual memory base address replaces the physical address in the configuration structure.

## Slide 41: XIicPs_Config *XIicPs_LookupConfig(u16 DeviceId)
Looks up the device configuration based on the unique device ID. A table contains the configuration info for each device in the system.
DeviceId contains the ID of the device to look up the configuration for.
Return
  A pointer to the configuration found or
  NULL if the specified device ID was not found.

## Slide 42: XIicPs_MasterRecvPolled() – to read from an I2C device
int XIicPs_MasterRecvPolled(XIicPs *InstancePtr, u8 *MsgPtr,
int ByteCount, u16 SlaveAddr);
InstancePtr is a pointer to the XIicPs instance.
MsgPtr is the pointer to the receive buffer.
ByteCount is the number of bytes to be received.
SlaveAddr is the address of the slave we are receiving from.
Return
  - XST_SUCCESS if everything went well.
  - XST_FAILURE if timed out.
MsgPtr[0] receives the 1st byte, MsgPtr[1] receives the 2nd byte, etc.

## Slide 43: XIicPs_MasterSendPolled() – to write to an I2C device
int XIicPs_MasterSendPolled(XIicPs *InstancePtr, u8 *MsgPtr, int ByteCount, u16 SlaveAddr)
InstancePtr is a pointer to the XIicPs instance.
MsgPtr is the pointer to the send buffer.
ByteCount is the number of bytes to be sent.
SlaveAddr is the address of the slave we are sending to.
return
  - XST_SUCCESS if everything went well.
  - XST_FAILURE if timed out.

## Slide 44: XIicPs_SetSClk()
int XIicPs_SetSClk(XIicPs *InstancePtr, u32 FsclHz)
InstancePtr is a pointer to the XIicPs instance.
FsclHz is the clock frequency in Hz. The two most common clock rates are 100KHz and 400KHz.
return
  - XST_SUCCESS if options are successfully set.
  - XST_DEVICE_IS_STARTED if the device is currently transferring data. The transfer must complete or be aborted before setting options.
  - XST_FAILURE if the Fscl frequency can not be set.
The clock can not be faster than the input clock divide by 22.

## Slide 45: xiicps_hw.h – Hardware Definition File
Addresses of all I2C module registers are defined
#define XIICPS_CR_OFFSET0x00 /**< 32-bit Control */
#define XIICPS_SR_OFFSET0x04 /**< Status */
#define XIICPS_ADDR_OFFSET0x08 /**< IIC Address */
#define XIICPS_DATA_OFFSET0x0C /**< IIC FIFO Data */
#define XIICPS_ISR_OFFSET0x10 /**< Interrupt Status */
#define XIICPS_TRANS_SIZE_OFFSET0x14 /**< Transfer Size */
#define XIICPS_SLV_PAUSE_OFFSET0x18 /**< Slave monitor pause */
#define XIICPS_TIME_OUT_OFFSET0x1C /**< Time Out */
#define XIICPS_IMR_OFFSET0x20 /**< Interrupt Enabled Mask */
#define XIICPS_IER_OFFSET0x24 /**< Interrupt Enable */
#define XIICPS_IDR_OFFSET0x28 /**< Interrupt Disable */

## Slide 46: xiicps.h – I2C Driver Header File
#define XIICPS_CR_OFFSET0x00 /**< 32-bit Control */
#define XIICPS_SR_OFFSET0x04 /**< Status */
#define XIICPS_ADDR_OFFSET0x08 /**< IIC Address */
#define XIICPS_DATA_OFFSET0x0C /**< IIC FIFO Data */
#define XIICPS_ISR_OFFSET0x10 /**< Interrupt Status */
#define XIICPS_TRANS_SIZE_OFFSET0x14 /**< Transfer Size */
#define XIICPS_SLV_PAUSE_OFFSET0x18 /**< Slave monitor pause */
#define XIICPS_TIME_OUT_OFFSET0x1C /**< Time Out */
#define XIICPS_IMR_OFFSET0x20 /**< Interrupt Enabled Mask */
#define XIICPS_IER_OFFSET0x24 /**< Interrupt Enable */
#define XIICPS_IDR_OFFSET0x28 /**< Interrupt Disable */

## Slide 47: I2C Controller of Zynq 7000
Chapter 20 I2C Controller, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585 (v1.10) February 23, 2015
I2C bus specification version 2
Supports 16-byte FIFO
Programmable normal and fast bus data rates
Master Mode
  Write transfer
  Read transfer
  Extended address support
  Support HOLD for slow processor service
  Supports TO interrupt flag to avoid stall condition
Slave Monitor Mode
Chapter 20, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 48: I2C Controller of Zynq 7000
Slave Mode
  Slave transmitter
  Slave receiver
  Fully programmable slave response address
  Supports HOLD to prevent overflow condition
  Supports TO interrupt flag to avoid stall condition
Software can poll for status or function as interrupt-driven device
Programmable interrupt generation
Chapter 20, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 49: I2C Controller System Block Diagram of Zynq 7000
Each Cortex-A9 processor has a standard 32-bit APB slave port that operates at the CPU_1x clock Frequency
APB (Advanced Peripheral Bus) low bandwidth control accesses, for example register interfaces on system peripherals. Similar to AHB, but a much reduced, low complexity signal list.
Two I2C Controllers: I2C 0 and I2C 1
SCL and SDA can be connected from MIO or EMIO
SCL_T
Chapter 20 I2C Controller, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 50: Master Mode of I2C Controller of Zynq 7000
An I2C transfer can only be initiated by the APB host and two types of transfers can be performed.
  Write transfer, where the I2C becomes master transmitter
  Read transfer, where the I2C becomes master receiver
Control Register
TX Data Register
RX Data Register
Slave Address Register
Status Register
Chapter 20 I2C Controller, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 51: Register Overview
Chapter 20, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 52: The PS Clock Subsystem of Cortex A9
cpu_6x4x clock is used by CPU and SCU
  CPU – Central Processing Unit
  SCU – Snoop Control Unit
cpu_3x2x clock are used by OCM
  OCM – One Chip Memory unit
cpu_2x clock are used by AXI
cpu_1x clock are used by slower buses such as the Advanced Peripheral Bus. CPU_1X clock is 4 times slower than CPU core clock
Chapter 25 Clock, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 53: Base Clock and PS Peripheral Clock Control of Zynq 7000
Most peripheral controllers use cpu-1x clock
Except for DMAC
Chapter 25 Clock, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585

## Slide 54: Clock Generator of I2C Controller of Zynq 7000
In slave mode, the clock enable is used to extract synchronization information for correct sampling of the SDA line.
In master mode, the clock enable is used to establish a time base for generating the desired SCL frequency.
Zybo CPU clock is 640MHz, therefore cpu_1x clock is 160MHz
Chapter 20 I2C Controller, Zynq-7000 All Programmable SoC, Technical Reference Manual, UG585